## Slide 1
Session 5.1: Off-Site Solutions Deep Dive
Understanding DPPA Mechanisms

## Slide 2
Follow the Money: From your EVN Bill to a Bankable DPPA
# | Module
1 | The Baseline: What You Pay EVN Today
2 | Virtual DPPA Money Flow: The Five-Line Bill
3 | CfD Mechanics: What Drives Your Quoted Price
4 | Developer Economics and the Three Gates
5 | Case Studies 5 & 6
6 | Key Decision Points and Wrap-up
By the end of this session you will be able:
1. Breakdown a virtual DPPA monthly settlement into its five components and compare it to your EVN bill
2. Explain how the CfD strike, market price (FMP), loss factors, and grid fees set your net cost
3. See why buyers, sellers and lenders each have a “gate” and why a deal must pass all three
4. Leave with realistic pricing expectations grounded in a real factory model
Scope: Virtual DPPA (grid CfD) only.
Session Roadmap

## Slide 3
Module 1:
The Baseline: What You Pay EVN Today

## Slide 4
Period | Hours | Versus Base
Off-peak | 00:00 - 06:00 | ~0.52x
Normal | 06:00 - 18:00 | 1.0x
Peak | 18:00 - 23:00 | ~1.78x
Sunday rule: no peak period on Sundays (all hours normal).
Voltage | Off-peak | Normal | Peak
>=110kV | 0.034 | 0.065 | 0.116
22-110kV | 0.037 | 0.070 | 0.126
6-22kV | 0.042 | 0.079 | 0.141
<6kV | 0.049 | 0.092 | 0.164
Why this matters for DPPA
Every DPPA offer is judged against this bill: “business-as-usual” (BAU)
Peak hours cost 3.4x off-peak: your load shape decides what "average" means for you
Residual energy (load not covered by the DPPA) keeps paying these TOU rates
The savings benchmark
BAU = your current EVN bill escalated ~4%/yr (historical trend 2015-2024)
A DPPA is evaluated on cumulative cost vs BAU over 10 years and over the project lifetime - not just Year 1
EVN tariff escalation is the main source of long-term DPPA value
(USD/kWh approx. 2025)
Module 1 - The Baseline
What You Pay EVN Today: TOU Is The Reference Price

## Slide 5
Module 2:
Virtual DPPA Money Flow: The Five-Line Bill

## Slide 6
Module 2 - The Five-Line Bill
Virtual DPPA Money Flow: Three Relationships, One Bill
RE GENERATOR
sells 100% of output
to the spot market
VWEM SPOT MARKET
pays generator FMP
per kWh generated
EVN
meters, wheels, & bills
the DPPA customer
YOUR FACTORY
pays EVN the DPPA bill;
settles CfD with generator
energy -> market (FMP)
DPPA bill (5 lines)
CfD settlement (two-way)
Physical electrons flow through the national grid as usual and the DPPA is a financial overlay
The generator's revenue = spot sales at FMP + CfD settlement with your factory
Your factory cost = the five-line EVN bill + the CfD settlement

## Slide 7
Module 2 - The Five-Line Bill
Virtual DPPA Money Flow: Three Relationships, One Bill
RE GENERATOR
sells 100% of output
to the spot market
VWEM SPOT MARKET
pays generator FMP
per kWh generated
EVN
meters, wheels, & bills
the DPPA customer
YOUR FACTORY
pays EVN the DPPA bill;
settles CfD with generator
energy -> market (FMP)
DPPA bill (5 lines)
CfD settlement (two-way)
Physical electrons flow through the national grid as usual and the DPPA is a financial overlay
The generator's revenue = spot sales at FMP + CfD settlement with your factory
Your factory cost = the five-line EVN bill + the CfD settlement
CFD
Electricity Flows
Electricity Flows
Pays FMP per kWh
Electricity Flows
Financial Flows

## Slide 8
Module 2 - The Five-Line Bill
The Monthly DPPA Settlement Has Five Lines
# | Line | Formula | Level (2025 reference)
1 | Market energy | Q_Khc x FMP x k x K_pp | FMP avg ~1,426.6 VND/kWh; k~1.026; K_pp by voltage
2 | DPPA service fee | Q_Khc x C_dppa_dv | 360 VND/kWh
3 | Balancing fee | Q_Khc x P_cl | 163.3 VND/kWh
4 | Residual purchase | (Load - Q_Khc) x EVN retail | TOU rates
5 | CfD settlement | (Strike - FMP) x min(Q_c, Q_Khc) | Two-way: can be + or -
Lines 1-4 are billed by EVN. Line 5 settles bilaterally with the generator under CfD contract.
Q_Khc = the renewable volume actually received and consumed (defined next slide).
CFMP = FMP x k: k converts the market price to the customer delivery point (price conversion, not a volume loss).

## Slide 9
Module 2 - The Five-Line Bill
Contracted Volumes & Actual Electricity Consumption
Q_adj = Q_meter / K_pp delivered volume at your meter
Q_Khc = min(Load, Q_adj) settled volume (lines 1-3)
Q_CfD = min(Q_c, Q_Khc) CfD settles on received volume
Grid losses are reflected through coordinated volume and price conversions: K_pp converts generator-meter output into buyer-side credited volume, while k and K_pp convert FMP into the corresponding buyer-side market-energy price.
If the plant generates more than you consume in an hour, the excess earns the generator spot revenue only; it is NOT billed to you and does NOT earn CfD
Practical consequence: Contracted volume (Q_c) above your real consumption buys nothing
Which volume? You settle only on what you actually consume

## Slide 10
Module 2 - The Five-Line Bill
Simulation: Industrial Park Buys 6,000 MWh/month
Parameter | Symbol | Value
Consumption = received RE volume | Q_KH = Q_Khc | 6,000,000 kWh/mo
Contracted CfD volume | Q_c | 6,000,000 kWh/mo
CfD strike price | P_c | 1,300 VND/kWh
Market price (monthly avg) | FMP | 1,200 VND/kWh
Price conversion factor | k | 1.026
Loss factor (110 kV) | K_pp | 1.008
DPPA service fee | C_dppa_dv | 360 VND/kWh
Balancing fee | P_cl | 163.3 VND/kWh
Avg retail price (residual) | P1 | 2,204 VND/kWh
Scenario
A 50 MW solar plant contracts its full output to one industrial customer
Consumption exactly equals delivered RE volume - no residual EVN purchase this month
Strike just 100 VND above market - watch what the fees do
Source: EAVCED public training

## Slide 11
Module 2 - The Five-Line Bill
The Five Lines, Computed
Line | Calculation | VND/month
1. Market energy (C_DN) | 6,000,000 x 1,200 x 1.026 x 1.008 | 7,446,297,600
2. Service fee (C_dppa) | 6,000,000 x 360 | 2,160,000,000
3. Balancing fee (C_cl) | 6,000,000 x 163.3 | 979,800,000
4. Residual (C_bl) | 0 kWh x 2,204 | 0
EVN bill (C_EVN) | lines 1 + 2 + 3 + 4 | 10,586,097,600
5. CfD settlement (C_CfD) | (1,300 - 1,200) x 6,000,000 | 600,000,000
TOTAL (C_KH) | C_EVN + C_CfD | 11,186,097,600
Effective cost = 11,186,097,600 / 6,000,000 = ~1,864 VND/kWh for fully renewable supply (versus ~2,204 VND avg retail in the example)
Generator side: 6,048,000 kWh x 1,200 (spot) + 600,000,000 (CfD) = 7,857,600,000 VND

## Slide 12
Virtual DPPA is rarely a Day-1 discount. Its value comes from price certainty versus EVN escalation, being able to cover 100% of annual electricity demand with contracted renewable generation, and utilizing credible renewable claims.
Component (per matched kWh) | VND/kWh | USD/kWh (cents)
Market energy at 2025 avg FMP x k x K_pp (22-110kV) | ~1,504 | ~6.0
DPPA service fee (C_dppa_dv) | 360 | 1.4
Balancing fee (P_cl) | 163.3 | 0.7
Delivered cost before CfD | ~2,027 | ~8.1
The 523 VND/kWh of fixed fees applies to every matched kWh, regardless of your strike
They are set by regulation, not negotiation
Compare ~2,027 VND delivered (pre-CfD) with your own TOU mix - for many factories that is already near or above average grid cost
Module 2 - The Five-Line Bill
Your Monthly Settlement Has Five Lines

## Slide 13
Module 3:
CfD Mechanics: What Drives Your Quoted Price

## Slide 14
Module 3 - CfD Mechanics
The CfD Is Two-Way: Certainty, Not Automatic Savings
CfD cash flow = (Strike - FMP) x Q_CfD
Market condition | Who pays whom
FMP below strike | You top up the generator
FMP above strike | Generator pays you back
Net effect: the renewable energy cost is locked near the strike (+ fees), whatever the market does
2025 reference: FMP averaged ~1,427 VND/kWh with strong hourly volatility; the CfD removes that volatility from the budget
A strike below expected average FMP would mean expected receipts, but no developer can finance that (Module 4)

## Slide 15
Module 3 - CfD Mechanics
Strike Escalation & The Year 1 Reality
Strike escalation (e.g., 4%/yr)
Escalating strikes improve the seller's and lender's lifetime economics...
...but do nothing for the Year 1 cost and compound against BUYER later
Negotiate the escalation index as hard as the starting strike (fixed VND vs CPI vs USD-linked)
What Year 1 usually looks like
In most realistic structures, Year 1 DPPA cost is at or above BAU
Savings build as EVN tariffs escalate (~4%/yr) against BUYER locked strike
→ Advice: Evaluate on 10-year and lifetime cumulative cost, not on Year 1 alone
Internal Budget Question to Consider: Can we accept a modest Year 1 premium to cap 15~25 year exposure?

## Slide 16
Module 3 - CfD Mechanics
Contract Volume VS Your Load Shape
Solar generation peaks midday, but the factory runs its own shape. The overlap—hour by hour - is what matters most.
If you... | Then… | Cost consequence
Over-contract (Q_c > consumption) | CfD caps at consumed volume - excess earns nothing | You paid contract terms for volume you can’t settle
Match contract to hourly overlap | Every contracted kWh settles | Efficient; this is the target
Under-contract (Q_c < overlap) | More residual purchased from EVN at TOU | Less price certainty, smaller renewable claim
Ask every developer for an hourly (8760 hour) matching analysis against your meter data, not an annual percentage
Batteries can shift the overlap window but add CAPEX the tariff must carry (see the case study)

## Slide 17
Module 4:
Developer Economics and the Three Gates

## Slide 18
Module 4 - Developer Economics
Developer’s Perspective on Economics
Revenue =
Q_meter x FMP spot sales (volatile) +
(Strike - FMP) x Q_CfD
CfD with your factory (stabiliser)
The CfD converts volatile spot revenue into a near-fixed price on matched volume
Your strike IS the developer's bankable revenue line
Everything the lender checks flows from it
Capital Structure | 70% Debt / 30% Equity
Debt Term | ~10 years
Debt Interest Rate (VND) | ~8.5% per year
Debt Interest Rate (USD) | ~5% per year (International)
Equity Target Return | 12 - 15%+ IRR
CIT Incentives | 4 years exempt + 9 years at half rate

## Slide 19
Module 4 - Developer Economics
A Deal Must Pass Three Gates to Proceed
Gate | Who | Test | Strike pressure
1. Buyer | You | Cumulative cost <= BAU over 10 yr AND lifetime | Pushes strike DOWN
2. Seller | Developer | Equity IRR >= 12-15% | Pushes strike UP
3. Lender | Bank | Minimum DSCR >= ~1.20x every year | Pushes strike UP (hardest gate)
DSCR = , computed for every year of the loan
One CAPEX heavy year ( e.g., a battery replacement) can sink the whole financing even if averages look fine
The negotiation window is the strike range where all three gates “pass”; but it can be empty (see case study)
A strike below the developer's bankability floor does not mean a cheap deal;
it means no project.
THREE GATES
Debt Service
Cash available for Debt service

## Slide 20
Module 4 - Developer Economics
Key Lifecycle Items The Tariff Must Contain
Item | Typical assumption | Buyer Implication
PV degradation | ~0.5%/yr output decline | Matched volume shrinks; lost kWh repurchased from EVN at TOU
Battery replacement | Large capex every 8-10 years | Can highly impact DSCR in that replacement year
CIT holiday | 4 yr exempt + 9 yr half rate (RE projects) | Improves developer economics
FX exposure | VND strike vs USD capex/debt | USD-linked terms shift FX the risks; price it consciously
The above terms are key components of the tariff and are included even when they are absent from the term sheet
These rarely appear in headline term sheets, but each one moves the bankable strike floor and therefore your price.

## Slide 21
Module 5:
Case Studies 5 & 6

## Slide 22
Module 5 - Case Study
Same Factory As Yesterday - Now Procuring Offsite
Yesterday’s On-Site Session: Cases 1-4 explored rooftop solar + BESS behind the meter.
Today: The same southern Vietnam manufacturing facility (22-110kV) signs a virtual DPPA with a dedicated solar + storage project.
Case 5: Solar + Large BESS
Case 6: Solar + Minimum BESS
Deal frame (both cases) | Value
DPPA type | Virtual (grid CfD) under Decree 57/2025
Strike price | 2,000 VND/kWh, escalating 4%/yr
Tenor / analysis period | 25 years
Financing | 70% debt, 8.5% VND, 10-yr term
Method | Full 8760-hour settlement simulation (ND57 formulas, hourly FMP/CFMP series) + 25-year project cash-flow model with the three gates.

## Slide 23
Metric | Result
Seller equity IRR | 16.9%
Project IRR | 13.5%
Developer NPV | $1.52M
Minimum DSCR | 1.14x (replacement year)
Payback | 9.1 yr
Buyer vs BAU - Year 1 | -8.7%
Buyer vs BAU - 10-yr cumulative | -8.9%
Buyer vs BAU - lifetime | -9.3%
At strike 2,000 the buyer pays ~9% MORE than BAU on every horizon
The oversized battery adds a ~$1.2M replacement around year 11 that the tariff must recover
Even so, lender comfort is thin (min DSCR 1.14x < 1.20x)
Lesson 1: An oversized battery cannot carry its own replacement cost through the tariff; everyone loses.
BATTERY EATS THE DEAL
Module 5 - Case Study
Case Study 5: Solar + Large BESS

## Slide 24
Metric | Result
Seller equity IRR | 26.9%
Project IRR | 18.2%
Developer NPV | $2.54M
Minimum DSCR | 1.50x (comfortably > 1.20x)
Payback | 4.7 yr
Buyer vs BAU - all horizons | -14.4%
Lean sizing: seller and lender are now comfortable - returns strong, DSCR 1.50x
But at strike 2,000 VND/kWh the buyer is ~14% worse than BAU: the seller's headroom IS the negotiation space
Therefore, sweep the strike down and see where the gates cross
Lesson 2: Right-sized the BESS makes the project financeable. Then, the entire negotiation is the strike price.
CHALLENGING, YET BANKABLE
Module 5 - Case Study Case Study 6: Solar + Minimum BESS

## Slide 25
Module 5 - Case Study Sweeping The Strike On Case Study 6: Empty Window
56 scenarios analyzed: 12 strike prices ranging from 1,200-2,200 VND/kWh and 4 contract volumes ranging from 70-100%.
Gate results:
Strike level (VND/kWh) | Buyer gate | Seller gate | Lender gate (>=1.20x) | Balanced?
~2,000 (offer) | FAIL -14% | PASS | PASS 1.50x | No
~1,400 | FAIL -1.4% | PASS 19% | PASS 1.19-1.5x | No
~1,300 x 70% vol | PASS +0.5% lifetime | PASS 17.9% | FAIL 1.14x | No
~1,200 | PASS +2.9% | PASS | FAIL <1.20x | No
The buyer turns positive just as the lender drops out: 0 of 56 scenarios pass all three gates at current market prices and fee levels.
Pricing alone cannot balance this deal, BUT there are “levers” that can: lower leverage, debt sculpting, USD-denominated debt (~5%), fee relief, longer tenor.

## Slide 26
Module 5 - Case Study What This Means And Expectations
Expect low single-digit lifetime savings at best. The product you are buying is 10-25 year price certainty, meet up to 100% of annual electricity demand with contracted renewable generation, and utilize credible renewable claims, but all at a price premium.
Expect Year 1 to cost more than BAU. Plan the internal approval around cumulative horizons.
Strike offers near 2,000 VND/kWh leave the buyer deeply negative. Realistic buyer-positive territory starts near ~1,300 VND, which today fails the lender.
Deal feasibility is decided by financing structure as much as by price. Ask developers HOW their project is financed, not just what they charge.

## Slide 27
Module 6:
Key Decision Points and Wrap-up

## Slide 28
Module 6 - Decision Points
Five Questions That Change The Term Sheet
# | Decision | What to check
1 | Strike level & escalation/indexation | Fixed VND vs escalating/deescalating vs USD linked; model these vs BAU
2 | Contract volume vs load shape | 8760 hourly matching vs meter data; CfD caps at consumed volume
3 | Tenor & termination | Developer wants 15-25 yr; match to your lease / order book; exit terms
4 | Voltage eligibility & K_pp | >=22kV only today; which K_pp applies decides your loss adjustment
5 | Risk allocation | FMP volatility, curtailment, negative CfD months, change-in-law
Items 1-4 are quantifiable before negotiation; run them against load data first.